## Slide 1: Audio/Bumpbot
ECE-1001
Team: Kit #15
Member #1 - Barak Barclay
Member #2 - Jasen Curtis

## Slide 2: Abstract
Drivebot from lab #2
  Attached Sound-sensor
  Attached Touch-sensor
Use of LCD display
Use of Motor Commands
(Figure 1 - Taken from Barak’s phone)

## Slide 3: Practical uses
Vacuum
70 Sensors
Learns Layout of room
Does not re-vacuum

## Slide 4: introduction
Task #1 Sound-Level
  Display Sound Levels on LCD
    Clears LCD every 100 msec
Task #2 Clap Down and Back
  Hear Clap
    Drive Forward (5 sec), Turn 180 degrees,
    Return to Start and Turn 180 degrees

## Slide 5: Introduction
Task #3 Clap and Go
  Hear Clap
    Drive Forward (5 Sec), Turn 180 degrees, Return to Start
    Stop, Turn 180 degrees, Play Tone
  Repeat All
Task #4 Clap-Bump and Drive
  Hear Clap
    Drive Forward
  Touch Sensor pushed
    Stop motor, Display crash count, plays tone
    Backs up, Stops, Turns random angle, Stops
  Repeats everything but hearing clap

## Slide 6: Results
Task #1
  Used only one conditions for if statements
      if ((SensorValue(S1) <= 66)&&(SensorValue(S1) > 33))
Task #2
  Was not registering clap
      eraseDisplay();
      displayTextLine (1, "%d", SensorValue[S1]);
      wait1Msec(1000);

## Slide 7: Results
Task #3
  Instead of turning it was driving forward
    nSyncedMotors = synchAC;
    nSyncedTurnRatio = 100;
      Turn ratio set to -100
Task #4
  Bot would not continue after first bump
    Added a second while loop in between
      if (SensorValue[S1] > 35)
      {
      while (true)

## Slide 8: Conclusion
Remember multiple conditionals need to be used at times
Wait time for program to start to zero out sensor: Wait time command, Set sensor value to zero
Remember to set synch turn ratio negative for turns
Can include a while loop within in a while loop

## Slide 9: Questions?

## Slide 10: Reference
Figure one Taken from Barak’s phone.
M. Hanlon, “Dyson’s Robot Vacuum Cleaner – the DC06,” Gizmag., 2 June 2004.
D. Parker. (2007) [Online]. Available: http://www.nxtprograms.com/

## Slide 11: Appendix
Task 1
#pragma config(Sensor, S1, soundSensor, sensorSoundDB)
task main()
{
while(true)
{
eraseDisplay();
displayTextLine (1, "Sound Level:", SensorValue(S1));
if (SensorValue(S1) <= 33)
{
displayTextLine (2, "Quiet", SensorValue[S1]);
}
if ((SensorValue(S1) <= 66)&&(SensorValue(S1) > 33))
{
displayTextLine (2, "Noisy", SensorValue[S1]);
}
if ((SensorValue(S1) <= 100)&&(SensorValue(S1) > 66))
{
displayTextLine (2, "Loud", SensorValue[S1]);
}
wait1Msec (100); // Delay
}//while
}

## Slide 12: Appendix
Task 2
#pragma config(Sensor, S1, soundSensor, sensorSoundDB)
task main()
{
while (true)
{
eraseDisplay();
displayTextLine (1, "%d", SensorValue[S1]);
wait1Msec(1000);
if (SensorValue[S1] > 35)
{
motor[motorA]= 30; // Turn motor A on 50%
motor[motorC]= 30; // Turn Motor C on 50%
wait1Msec (5000); // Delay
bFloatDuringInactiveMotorPWM = false; //motors will brake when power is set to "0"
motor[motorA]= 0; // Turn Motor A off
motor[motorC]= 0; // Turn Motor C off
//for it to turn around exactly 180 degrees, sync motors
motor[motorA]= 30; // Turn motor A on 50% (Turn around)

## Slide 13: Appendix
motor[motorC]= -30; // Turn Motor C off
wait1Msec (1600); // Delay
motor[motorA]= 0; // Turn Motor A off
wait1Msec (500); // Delay
motor[motorA]= 30; // Turn motor A on 50%
motor[motorC]= 30; // Turn Motor C on 50%
wait1Msec (5000); // Delay
//for it to turn around exactly 180 degrees, sync motors
motor[motorA]= 30; // Turn motor A on 50% (Turn around)
motor[motorC]= -30; // Turn Motor C off
wait1Msec (1600); // Delay
motor[motorA]= 0; // Turn Motor A off
wait1Msec (500); // Delay
break;
} // end if
} //end while
}

## Slide 14: Appendix
Task 3
#pragma config(Sensor, S1, soundSensor, sensorSoundDB)
task main()
{
while (true)
{
eraseDisplay();
displayTextLine (1, "%d", SensorValue[S1]);
wait1Msec(1000);
if (SensorValue[S1] > 35)
{
nSyncedMotors = synchAC;
nSyncedTurnRatio = 100;
motor[motorA]= 30; // Turn motor A on 50%
wait1Msec (5000); // Delay
bFloatDuringInactiveMotorPWM = false; //motors will brake when power is set to "0"
motor[motorA]= 0; // Turn Motor A off
nSyncedTurnRatio = -100;
motor[motorA]= 30; // Turn motor A on 50% (Turn around)
wait1Msec (1600); // Delay

## Slide 15: Appendix
motor[motorA]= 0; // Turn Motor A off
wait1Msec (500); // Delay
nSyncedTurnRatio = 100;
motor[motorA]= 30; // Turn motor A on 50%
wait1Msec (5000); // Delay
nSyncedMotors = synchAC;
nSyncedTurnRatio = -100;
motor[motorA]= 30; // Turn motor A on 50% (Turn around)
wait1Msec (1600); // Delay
motor[motorA]= 0; // Turn Motor A off
wait1Msec (500); // Delay
playSound(soundUpwardTones); //Plays the sound "Upward Tones"
wait1Msec (2300); // Delay
} // end if
} //end while
}

## Slide 16: Appendix
Task 4
#pragma config(Sensor, S1, soundSensor, sensorSoundDB)
#pragma config(Sensor, S2, touchSensor, sensorTouch)
task main()
{
// In order to fix the sound sensor, and maybe the touch sensor, from reading wrong values at first
//Set a int temp =0;
//wait time then set int temp = SensorValue[S1];
//wait time
// also set if paramenters to react to temp instead of SensorValue
int degrees = 0;
int crash_count = 0;
degrees = rand() % (2800-800) + 800;

## Slide 17: Appendix Cont.
while (true)
{
eraseDisplay();
displayTextLine (1, "%d", SensorValue[S1]);
wait1Msec(1000);
if (SensorValue[S1] > 35)
{
while (true)
{
nSyncedMotors = synchAC;
nSyncedTurnRatio = 100;
motor[motorA]= 30; // Turn motor A on 50%
bFloatDuringInactiveMotorPWM = false; //motors will brake when power is set to "0"

## Slide 18: Appendix cont.
crash_count++;
displayTextLine (2, "%d", crash_count);
playSound(soundUpwardTones); //Plays the sound "Upward Tones"
motor[motorA]= 0; // Turn Motor A off
wait1Msec (1600); // Delay
motor[motorA]= -50; // Turn motor A on 50% (Turn around)
wait1Msec (1000); // Delay
nSyncedTurnRatio = -100;
motor[motorA]= 30; // Turn motor A on 50% (Turn around)
wait1Msec (degrees); // Delay
motor[motorA]= 0; // Turn Motor A off
wait1Msec (500); // Delay
} //end 2nd if

## Slide 19: Appendix Cont.
} //end 2nd while
} // end 1st if
} //end 1st while