## Slide 1
Weekly Update #2
Team Name: EM Drop the Microelectronics
Project Manager: Barak Barclay
Logistics & Finance Manager: Alicia Lawrence
Design Manager: Brian Griffen
Test Manager: Chris Sherwood
Sponsor: EM Microelectronic
Faculty Sponsor: Dr. Byeong Lee
22 March 2019

## Slide 2
    Problem: 9V Battery Low Voltage Detection
    Some products need to have their batteries replaced before the battery dies completely
    Our team must design a board that checks that voltage and broadcasts once the voltage is critical
    Broadcasts only when low
      Sends BT packet

## Slide 3
    Bluetooth Specifications
    Bluetooth Version 5.0
      EM9304
    Bluetooth Packet Type
      Non-connectable vs. Connectable
        Power Consumption vs. Need for Pairing
    EM9304
      Certified w/ FCC for wireless transmission
      Supports 1.5V & 3V batteries
        Low-power switching regulator

## Slide 4
    Battery Specifications
    Battery Power Consumption
      Reduction of less than 20%
    Battery Alternatives
      Alkaline vs. Lithium Ion
      Cost vs. Capacity
        Total part cost <$5 at 10,000 units
      Temperature Range?
      Size
        Inner vs. Outer Module
    Battery Dimensions (ANSI/ EC Standard)
      Max: 48.5mm x 26.5mm x 17.5mm
      Min: 48mm x 25mm x 15mm

## Slide 5
    System Block Diagram
    Battery powers entire system
    Need voltage stepped down for EM9304
    Some type of circuitry detects voltage or current from sense line to EM9304

## Slide 6
    System Block Diagram

## Slide 7
    Resistive Load
    To properly characterize battery we need an idea of load
    Loads vary between photoelectric, ionization, and combination detectors
Manufacturer | Model | Product | Type of value | Average Current [uA] | Load Resistance [kOhms]
ANSI | - | Battery | Spec | 209.3 | 43
Ultra Life | U9VL-X | Battery | Calculated | 13.7 | 657
First Alert | SA303 | Smoke Alarm | Measured | 7.3 | 1,233

## Slide 8
    Battery Characterization Tests
    Capacity – ability to store energy
    Internal Resistance – ability to deliver current
    Self-Discharge – describes mechanical integrity of battery over time

## Slide 9
    Lithium and Alkaline Battery Comparison
Circuit Response | Battery Capacity | Lithium Voltage (V) |  |  | Alkaline Voltage (V) |  | 
 |  | Max | Min | Delta | Max | Min | Delta
Sample Voltage | 100% to 75% | 9 | 8.5 | 0.5 | 9 | 7.8 | 1.2
Advertise Alert | 75% to 50% | 8.5 | 8.5 | 0 | 7.8 | 7.2 | 0.6
Smoke Alarm Beeping | 50% to 25% | 8.5 | 8.1 | 0.4 | 7.2 | 6.5 | 0.7
Battery Dead | 25% to 0% | 8.1 | 5 | 3.1 | 6.5 | 5 | 1.5

## Slide 10
    Spec Sheet
 | MIN | TYP | MAX
Power Supply (V) | 6 |  | 9.5
Temperature (C) |  | 25 | 60
Alert Voltage (V) |  |  | 
Current Consumption (uA) | 2.74 |  | 41.86
Sampling Interval (per Hour) |  | 1 | 
Advertising Interval (Hz) |  | 0.5 | 
Sampling Length (# of days?) |  |  | 

## Slide 11
    Plans for Next Week
    Test various batteries for IV curves
    Decide on a battery
    Decide on a percentage for the BLE advertisements to start
    Study published battery tests and models