## Slide 1
Weekly Update #2
Team Name: EM Drop the Microelectronics
Project Manager: Barak Barclay
Logistics & Finance Manager: Alicia Lawrence
Design Manager: Brian Griffen
Test Manager: Chris Sherwood
Sponsor: EM Microelectronic
Faculty Sponsor: Dr. Byeong Lee
22 March 2019

## Slide 2
    Problem: 9V Battery Low Voltage Detection
    Some products need to have their batteries replaced before the battery dies completely
    Our team must design a board that checks that voltage and broadcasts once the voltage is critical
    Broadcasts only when low
      Sends BT packet

## Slide 3
    Bluetooth Specifications
    Bluetooth Version 5.0
      EM9304
    Bluetooth Packet Type
      Non-connectable vs. Connectable
        Power Consumption vs. Need for Pairing
    EM9304
      Certified w/ FCC for wireless transmission
      Supports 1.5V & 3V batteries
        Low-power switching regulator

## Slide 4
    Battery Specifications
    Battery Current Consumption
      Reduction of less than 20%
    Battery Alternatives
      Alkaline vs. Lithium Ion
      Cost vs. Capacity
        Total part cost <$5 at 10,000 units
      Temperature Range?
      Size
        Inner vs. Outer Module
    Battery Dimensions
      Max: 48.5mm x 26.5mm x 17.5mm
      Standard: 48mm x 25mm x 15mm

## Slide 5
    System Block Diagram
    Battery powers entire system
    Need voltage stepped down for EM9304 which operates at 1.5 or 3.0 V
    Some type of circuitry detects voltage or current from sense line to EM9304

## Slide 6
    System Block Diagram

## Slide 7
    Resistive Load
    To properly characterize battery we need an idea of load
    Loads vary between photoelectric, ionization, and combination detectors
Manufacturer | Model | Product | Type of value | Average Current [uA] | Load Resistance [kOhms]
ANSI | - | Battery | Spec | 209.3 | 43
Ultra Life | U9VL-X | Battery | Calculated | 13.7 | 657
First Alert | SA303 | Smoke Alarm | Measured | 7.3 | 1,233

## Slide 8
    Battery Characterization Tests
    Use current source instrument to develop battery IV curves
    With IV curve data we can find ideal voltage to start advertising
    Need a reliable method to drain battery to certain percentages for tests

## Slide 9
    Plans for Next Week
    Test various batteries for IV curves
    Decide on a battery
    Decide on a percentage for the BLE advertisements to start
    Study battery tests, profiles, and models that have already been published

## Slide 10: Thank You for Listening
Any Questions?